## Slide 1
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
Goal of the Challenge
Run any Game on an HPC with Display
receive the input signals from a controller that is connected to an ECU
sendsits signals via a Zone Controller to the HPC using Eclipse Kuksa and optionally Open1722.
Everything on the HPC should be orchestrated via Eclipse Ankaios, monitored by the Ankaios Dashboard and can run on the upcoming Digital.auto E2E Makerkit.
Test the full functionality of the Game input with digital.auto playground.
Use Arduino Devices to execute your code and Inputs.
Use Raspberry Pis with Displays to show and run your games.
Vehicle.Chassis
Vehicle.Cabin
Vehicle.Body
Vehicle.Powertrain
Vehicle.Windshield

## Slide 2
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
Challenge Intro
Overview of (some) SDV Projects
Which SDV Project is for what?
Easy challenge example with tutorial

## Slide 3
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
Overview of (some) SDV Projects and which project is for what
Digital.Auto or Eclipse Autowrx is an open Initiative to create the next generation of software-defined vehicle experiences
Digital.auto Playground is to test and simulate your Ideas. Try out your Business logic or Game within the Browser with no other tools needed. But “just” a simulation. The deployment to Hardware is ongoing. You can create Velocitas Applications out of the playground with one click.
The Vehicle Signal Specification introduces a domain taxonomy for vehicle signals. VSS introduces a syntax for defining vehicle signals in a structured manner and builds a catalog of signals related to vehicles.  This is your interface data definition!
Velocitas brings you a full SDK for Vehicle Applications on top of the VSS data signal specification.
It works seamlessly together with the KUKSA.val databroker and digital.auto playground. The outcome of a Velocitas build is an executable OCI container which can be executed by docker, podman, kanto-cm or other container runtimes. You can deploy and manage it with Eclipse Ankaios.
KUKSA.val project is bringing you the databroker and the vehicle abstraction with its providers. This implements the basis for a faster and leaner development of Vehicle Applications.
With the KUKSA-python-SDK you can also directly try out things to access the vehicle data.

## Slide 4
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
Overview of (some) SDV Projects
Eclipse Ankaios provides workload and container orchestration for automotive High Performance Computing (HPC) software . While it can be used for various fields of applications, it is developed from scratch for automotive use cases and provides a slim yet powerful solution to manage containerized applications.
Open1722 is an implementation of the IEEE 1722 protocol, for streaming audio/video, tunneling CAN/LIN messages and enabling remote access to peripheral bus systems.
ThreadX is Eclipse Foundation's advanced industrial grade Real-Time Operating System (RTOS). It is designed specifically for deeply embedded, real-time, and IoT applications.
Arduino is an open-source electronics platform based on easy-to-use hardware and software. Arduino boards are able to read inputs - light on a sensor, a finger on a button, or a Twitter message - and turn it into an output - activating a motor, turning on an LED, publishing something online..
The Ankaios Dashboard ist the ui interface for Eclipse Ankaios project. It offers insights into a running ankaios cluster, allows for modification/deletion/creation of workloads and offers a dependency graph for easier understanding of the interdependencies between workloads
Dashboard

## Slide 5
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
Example E/E Architecture
High-Performance
Compute
Zone Gateway OR Controller
ECU
Sensor /
Actuator
Ethernet
CAN, CAN-FD, LIN, etc
Front Zone
Cabin Zone
Rear Zone
Vehicle Compute
IVI
G/C
G/C
G/C
VCU
G/C
IVI
Infotainment
G/C
VCU

## Slide 6
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
Cut down complexity to 3 Zones and add the “Game”
High-Performance
Compute
Zone Gateway OR Controller
ECU
Sensor /
Actuator
Ethernet
CAN, CAN-FD, LIN, etc
Front Zone
Central Zone
Rear Zone
Vehicle Compute
Display Control
Rear Zone Control
Sensor
Actor
VCU
G/C
IVI
Infotainment
Front Zone Control
Sensor
Actor
Central HPC
Input Player 1
Input Player 2
Points LED Player 2
Pong Game
Points LED Player 1
Input processing
Signal forwarding
Signal forwarding
Game „Pong“
2 Player Pong is shown on the display.
The input of Player 1 is at the front zone of the Vehicle. Player 2 is in Rear Zone. Both players have different inputs. E.g. Player 1 has a break and gas pedal. Player 2 has a small Joystick.
Both Players have a LED Stripe where their points are displayed.
Game is won as one Player has 8 points.

## Slide 7
Simulation
{
[“Eclipse SDV”],
[“Hackathon”],
[“Chapter Two”]
}
Play by Wire
What Projects/Technology can be used and where
High-Performance
Compute
Zone Gateway OR Controller
ECU
Sensor /
Actuator
Ethernet
CAN, CAN-FD, LIN, etc
Front Zone
Central Zone
Rear Zone
Vehicle Compute
Display Control
Rear Zone Control
Sensor
Actor
VCU
G/C
IVI
Infotainment
Front Zone Control
Sensor
Actor
Central HPC
Input Player 1
Input Player 2
Points LED Player 2
Pong Game
Points LED Player 1
Input processing
Signal forwarding
Signal forwarding
Development PC
Dashboard